Oxyfuel Welding and Cutting Equipment (chapt.30)

- What is the purpose of a pressure regulator?

- What may result if a pressure regulator is not used on the type of gas or pressure range for which it was designed?

- Describe how a single-stage regulator operates?

- Is the torch pressure always the same as the working gauge pressure? Why or why not?

- Why does the high pressure gauge on the regulator not always indicate the amount of gas in the cylinder?

- How does the operation of the safety relief valve differ from the operation of a safety disc valve?

- Describe the difference between an argon cylinder valve fitting and a carbon dioxide cylinder valve fitting.

- What is meant by regulator creep?

- Who can repair regulators?

- Why must the pressure be released from the regulator when work is finished?

- Why are combination welding and cutting torches considered to be more versatile?

- What is the advantage of using an injector-type mixing chamber?

- What should be done to the packing if the valve knob does not turn freely after it has been tightened to stop a leak?

- What may happen to the tip seat if it is incorrectly tightened?

- What can happen to a tip if it is excessively cleaned with a tip cleaner?

- What is the difference between a reverse flow valve and a flashback arrestor?

- What are Siamese hoses?

- Why must the pressure be bled off hoses when work is complete?

- What is the difference between a backfire and a flashback?

- Why is a neutral flame the most commonly used oxyacetylene flame used?

- What properties should a good leak-detecting solution have?

- Why must the oxygen cylinder valve be opened all the way to the top?

- How long should hoses be purged?

- What should be done with cylinders with leaking valve stems?

- How should the spark lighter be held to light the torch?

- Once the torch is lit, why must the acetylene flow be increased until the flame stops smoking before the oxygen is turned on for adjustment?

- What type of piping can be used for a manifold system?