Chapter 30 Quiz

Oxyacetylene Equipment

- The oxyacetylene process is a:

  - Welding process which produces fusion of metals by heating them with an arc.

  - Welding process which produces fusion of metals with the heat contained from resistance electrical current.

  - Gas process that uses intense heat from the burning of a fuel gas and oxygen to produce a weld.

  - Gas shielded process which produces welds with the heat of a tungsten electrode arc.

- The oxygen and acetylene cylinder valves should be cracked open just for a moment before attaching the regulator:

  - to remove dirt and foreign material from the valve seat

  - to make sure there is gas in the cylinders

  - to remove the water vapor in the cylinder

  - to make sure it is the right type of gas

- This part of the oxyacetylene welding equipment is used to reduce cylinder pressures to a working pressure.

  - Reverse flow check valve

  - Flashback arrestor

  - Striker

  - Regulator

- Which of the following regulator safety valves is spring loaded and can reset itself?

  - Cylinder valve

  - Safety disc valve

  - Torch valve

  - Safety relief valve

- What term do we use when a regulator builds pressure when not in used do to a leaking valve or damage to the diaphragm?

  - Creep

  - Crack the valve

  - Cover

  - MT

- Who should repair regulators?

  - Other students

  - Your dad

  - Mr. Dillon

  - Trained technicians

- Why is it necessary to release the pressure in the regulator when welding is completed?

  - Makes it nice for other to start fresh

  - Continuous pressure on the spring and diaphragm can cause damage

  - Next time it is turned on the pressure released can damage the diaphragm.

  - Both b and c

- When the torch pops and goes out, what term do we use?

  - Flashback

  - Soot

  - Backfire

  - Slag

- Why must the pressure be bled off when welding process is complete?

  - Conserve gas

  - Gases in hoses could migrate into the other hose and cause an explosion.

  - Old gas doesn’t work as well.

  - There may be a leak in the hose.

- Which type of flame is used because it adds nothing to the weld pool?

  - Carburizing flame

  - Neutral flame

  - Oxidizing flame

  - Pure acetylene flame

- What is used for leak detection?

  - Bucket of water

  - Open flame

  - Bic lighter

  - Soapy water

- For a neutral flame the ratio of oxygen and acetylene to be supplied to the torch is:

  - 5:1

  - 1:1

  - 4:1

  - 1:5

- How far do we open an oxygen cylinder valve?

  - 1 full turn

  - All the way

  - Until the dials move

  - Depends on how big the oxygen cylinder is.

- When changing out tips, it’s OK to use a monkey wrench to tighten tips? True or False

- What should be done with a leaking acetylene cylinder valve?

____________________________________________________________________

- What is the only appropriate tool to use to light the oxyacetylene torch?

  - Bic lighter

  - Match

  - Your friends torch

  - sparklighter