Chapter 31 Quiz

Oxyacetylene gases and metals

- What are the separate parts that make up an oxyacetylene flame?

  - Tip and feather

  - Inner cone

  - Outer envelope

  - Both b and c

- Why is it not safe to use acetylene above 15 psi?

  - The red hoses can not withstand more than 15 psi

  - Acetone will be forced through the regulator and hose

  - The regulator has a maximum pressure reading of 15 psi

  - Above the critical pressure an explosion may occur

- Where is the highest temperature produced in a neutral oxyacetylene flame?

  - Inner cone

  - 3” from the tip

  - The outer flame

  - The flame is the same temperature everywhere

- What is the major advantage of using propane or natural gas?

  - Lower cost compared to acetylene

  - Higher temperature flame than acetylene

  - Readily available

  - Both a and c

- Why should coat hangers not be used as gas welding filler metals?

  - Unknown metals and alloys

  - May have coatings on them

  - Not designed for welding purposes

  - All the above

- Explain the significance of the AWS filler metal classification RG45.

R stands for-

G stands for-

45 stands for-

- Which fuel gas is the most frequently used fuel gas?

  - Propane

  - Natural gas

  - Acetylene

  - None of the above

- The mixture of oxygen and acetylene produces a high heat and temperature flame that is widely used for all the following except:

  - Brazing

  - Heating

  - Welding

  - Arc welding

- This is colorless, and is lighter than air, and has a strong garlic smell.

  - Oxygen

  - Argon

  - Acetylene

  - CO2

- This is used inside acetylene cylinders to absorb gas and to make it more stable. It absorbs acetylene in the same manner as water absorbs carbon dioxide in a carbonated drink.

  - Propane

  - Oxygen

  - Acetone

  - Cola

- What is the approximate temperature of an oxyacetylene flame?

  - 212ºF

  - 2200ºF

  - 5600ºF

  - 10000ºF

- Most fuel gases used for welding are _______________, gases made up from  hydrogen and carbon.

- List the three types of oxyacetylene flames.

- ____________________________________________

- ____________________________________________

- ____________________________________________