Flame Cutting

Chapter 7

- Using Table 7-1, list the six different fuel gases in rank order according to their temperature.

- What is a combination welding-cutting torch?

- State one advantage of owning a combination welding-cutting torch as opposed to just having a cutting torch.

- State one advantage of owning a dedicated cutting torch as compared to having a combination welding-cutting torch.

- What is a mixing chamber? Where is it located?

- Define the term equal-pressure torch. How does it work?

- How does an injector-type mixing chamber work?

- State the advantage of having two oxygen regulators on a machine-cutting torch.

- Why are some copper alloy cutting tips chrome plated?

- What determines the amount of preheat flame requirements of a torch?

- What can happen if acetylene is used on a tip designed to be used with propane or other such gas?

- Why are some propane and natural gas tips made with a deep, recessed center?

- What types of tip seals are used with cutting tips?

- If a cutting tip should stick in the cutting head, how should it be removed?

- How can cutting torch tip seals be repaired?

- Why is the oxygen valve turned on before starting to clean a cutting tip?

- Why does the preheat flame become slightly oxidizing when cutting lever is released?

- What causes the tiny ripples in a hand cut?

- Why is a slightly forward torch angle helpful for cutting?

- Why should cans, drums, or other sealed containers not be opened with a cutting torch?

- Why is the torch tip raised as the cutting lever is depressed when cutting a hole?

- Why are the preheat holes not aligned in the kerf when making a bevel cut?

- Sketch the proper end shape of a soapstone that is to be used for marking metal.

- Using Table 7-4, answer the following:

  - Oxygen pressure for cutting ¼” thick metal

  - Acetylene pressure for cutting1” thick metal

  - Tip cleaner size for a tip for 2” thick metal

  - Drill size for a tip for ½” thick metal

- What is the best way to set the oxygen pressure for cutting?

- What metals can be cut with the oxyfuel gas process?

- Why is it important to have ventilation and/or a respirator when cutting some used metal?

- What factors regarding a cut can be read from the sides of the kerf after a cut?

- What is hard slag?

- Why is important to make good-quality cuts?

- Describe the methods of controlling distortion when making cuts.

- How does cutting small diameter pipe differ from cutting large diameter pipe?