Pedestal Grinder Safety Guidelines

- Always wear safety glasses when operating a grinder or wire buffer.

- Don’t wear any jewelry. Remove your watches, rings, bracelets or necklaces.

- Never use the side of the wheel for grinding. Always grind on the face of the wheel.

- One person uses the grinder at a time.

- The area around the grinder must be clear and clean.

- Use pliers or vise-grips to hold small objects or parts. Don’t hold small objects with your fingers when you

grind; your fingers will be dangerously close to the wheel. Also, small objects can be pulled in the area between the wheel and the tool rest, and draw your fingers into the wheel.

- Loose clothing can get caught in the grinder. Keep clothes tucked in and keep shirt sleeves buttoned down or rolled up neatly out of the way.

- If your hair is long, wear a cap over it. Long hair can get caught in the grinder. Tuck your hair neatly under a cap.

- Before turning on the grinder, check the wheel. The grinding stone must be in good condition and clean. Don’t use the grinder if the wheel is worn, damaged, cracked, clogged or defective in any way. If there’s anything wrong with the grinder, tell your instructor; don’t use it. (don’t grind soft materials-aluminum, brass, or wood)

- Always use the tool rest. Never try to grind free-handed. Be sure the tool rest is adjusted properly. The tool rest should be adjusted for the correct angle and it should be set close to the wheel. The tool rest should be 1/8” from the face of the wheel. The top guard is 3/16”.

- If you need to adjust the tool rest, make the adjustments with the grinder turned off and completely stopped.

- Check the coolant pan to be sure there is water in it. Parts should be dipped in water if they become to hot to handle.

- Stand to one side when you switch on the grinder. Stand off to one side until it comes up to full speed. If a wheel is damaged or defective, it can fly apart as it comes up to full speed.

- If the grinder starts to shake or vibrate, or if it doesn’t sound right, move to one side and turn it off immediately.

- Keep your hands and fingers away from the wheel while it is moving.

- When the job is complete, shut off the grinder and let it coast to a stop. Never grind when the machine is coasting.

- Wash your hands to remove the grains of abrasive and metal particles. Don’t touch your face or eyes until you have washed.

Pedestal Grinder Safety Test

1.  Always wear __________ or goggles when you operating a grinder or a wire wheel.

2.  __________ such as watches, necklaces, rings or bracelets should not be worn when you use the grinder or buffer.

3.  Never wear __________ clothing when you are around power equipment.

4.  Wear a __________ and keep your hair tucked neatly under it to keep it from getting caught in the grinder.

5.  Don’t use the grinder if the wheel is worn, damaged, cracked, clogged or __________ in any way.

6.  Never try to grind free-handed.  Always use the __________ on the grinder.  It should be 1/8” from the face of the wheel.

7.  If you need to adjust the tool rest, the grinder must be switched off and completely __________.

8.  Check the_________ to be sure there is water in it.

9.  Don’t stand in front of the wheel when you switch on the grinder.  Stand to __________ and wait until it comes up to full speed before you use it.

10.  If the grinder begins to vibrate, or if it doesn’t sound right, move to one side and turn it off __________.

Name:                                       Date:

A.  Damaged

B.  Loose

C.  Safety Glasses

D.  Coolant Pot

E.  Stopped

F.  Immediately

G.  Jewelry

B.  The Side

I.  Tool Rest

J.  Cap

Pedestal Grinder Safety Test

100% Required

1. Safety glasses must be worn while grinding

A. stainless steel.

B. aluminum.

C. steel.

D. any material.

2. The maximum space between the tool rest and the wheel is

A. 3/32”.

B. 3/16”.

C. 1/8”.

D. 3/32”

3. After turning off the grinder you should

A. push the metal against the wheel.

B. engage the brake drum.

C. use the dressing tool to clean the wheel.

D. walk away.

4. The work should be dipped frequently to

A. prevent oxidation.

B. preserve the metals temper.

C. anneal the metal.

D. cool the metal.

5. The maximum distance for the top guard is

A. 1/8’.

B. 3/16’.

C. 3/32”

D. 3/8”.

6. When grinding you should concentrate on

A. the time clock.

B. what’s for lunch.

C. the instructor.

D. the job.

7. What kind of movement should the operator use to prevent grooves forming.

________________________________________________________

8. When grinding, the floor and surrounding area should be

A. painted and sealed.

B. cemented.

C. free from obstructions and clean.

D. covered with non-skid grates.

9. You should never use the pedestal grinder to grind

A. wood products.

B. aluminum.

C. brass.

D. all the above.

10. If the wheel is clogged, uneven, or grooved you should use

A. at your own risk.

B. ask for a new wheel.

C. a piece of carbide.

D. a dressing tool.

11. If the grinder isn’t running smoothly (starts to vibrate or shake)

A. continue to grind, figure it out later.

B. dress the wheel.

C. ask another student to check it out.

D. turn off and ask Mr. Dillon for help.

12. Before using the grinder you should inspect

A. the floor.

B. the wheels.

C. the guards.

D. all the above.

13. When starting the grinder you should

A. stand in front of the wheel.

B. check for fellow students safety.

C. stand aside until the grinder reaches full r.p.m.

D. both B and C.

14. True/False	Loose clothing or long hair can be dangerous around the pedestal grinder.

15. True/False	The side of the grinding wheel should never be used.

I will use equipment safely and demonstrate safe work practices.

Student Name:______________________  Date:_____________